## Slide 1: CCNA (200-125)
Cisco Router’s Basic Configuration
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2
Lecture Overview
Cisco Router’s Basic Configuration
Working Modes Of a Router:
User Mode (Default mode)
Privilege or Administrative Mode
Global Configuration Mode
Interface Configuration Mode
5. Line Configuration Mode
6. Router Mode
7. Sub-Interface Mode

## Slide 3
Router> is the user mode, i.e the default prompt. It means that when ever a router boots successfully it lands into the user mode. Router cannot be configured from this mode, but it is used for just monitoring purpose.
USER MODE

## Slide 4
Router# it is the administrating mode, we can check whether the settings and configurations made have been implemented or not.
Router> en (Press enter)--- to activate privilege mode
Router #
Router # Sh int e0
If it is new router all the interfaces are by default shut down, so the message will be, “ Ethernet 0 is administratively down, line protocol is down.”
PRIVILEGE MODE

## Slide 5
Router# Config t
Router (Config)#
Global Configuration Mode
As the name indicates, it is a global configuration mode i.e. we can configure any interface from this mode, just by entering into the interface mode.

## Slide 6
The “Clock” Command
The clock command is used to set the clock of Router.
Syntax.
Router# clock set hh:mm:ss Day of week Month Year
E.g.
Router#clock set 16:35:00 1 April 2003
Note* This is the only configuration which can be done from privilege mode,every other configuration should be done at global configuration mode only.

## Slide 7
Some important show commands in privilege mode
Router# sh clock
sh int (interface name eg e0)
Sh history
Sh memory
Sh running-config
Sh startup-config
To save configuration from RAM TO NVRAM
Router#Copy Running-config Startup-config (or)
Router#Write Memory

## Slide 8
To configure Hostname (or) Identification of Router over the network.
Router#conf t
Router(config)#Hostname R_2503
R_2503(config)#^Z

## Slide 9
Router Password Configuration
User Mode Password
Privilege Password
Virtual Terminal (Virtual Teletype) Password
Console Password
Auxiliary Password

## Slide 10
PASSWORDS
Enable Password
Enable Secret
Enable Password:- It is global command restricts access to the user mode, the password is in clear text.
Router(config)#Enable password 123
Enable Secret:- It is global command restricts access to the privillege mode Here the password is in encrypted form.
Router(config)#Enable secret cisco

## Slide 11
Virtual Terminal Password
It establishes a login password on incoming Telnet sessions.
Router#conf t
Router(config)#Line vty 0 4
Router(config-line)#Login
Router(config-line)#password cisco
Router(config-line)#^Z

## Slide 12
Console Password
It establishes a login password on the console terminal.
Router#conf t
Router(config)#Line Console 0
Router(config-line)#Login
Router(config-line)#Password cisco
Router(config-line)#^Z

## Slide 13
Auxiliary Password
It establishes a login password to remote administration.
Router#conf t
Router(config)#Line Aux 0
Router(config-line)#Login
Router(config-line)#Password cisco
Router(config-line)#^Z

## Slide 14
CONFIGURING INTERFACES
LAN interface (ETHERNET Port)
WAN interface (SERIAL Port)

## Slide 15
ETHERNET
Router(config)#Interface Ethernet 0
Router(config-if)#Ip Address 200.150.1.254 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#^Z
Router#Show Int E0

## Slide 16
SERIAL
Router(config)#Interface Serial 0
Router(config-if)#Ip Address 150.10.1.1 255.255.0.0
Router(config)#clock rate 56000
Router(Config-if)# bandwidth 64
Router(config-if)#No shutdown
Router(config-if)#^Z

## Slide 17
Interpreting The Interface Status
Router# show int s0
Serial0 is up, line protocol is up.
Is the message if the interface is operational.
Serial0 is up, line protocol is down
This is if there is any connection problem.
Serial0 is down, line protocol is down
This is if there is any interface problem.
Serial0 is administratively down, line protocol is down….. This is if the interface is disabled.