## Slide 1: CCNA (200-125)
Disaster Recovery
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture-7 Overview
Disaster Recovery
  Rom Monitor
  Cisco Router’s Password Recovery

## Slide 3: Disaster Recovery – ROM Monitor
ROM Monitor is very helpful in recovering from emergency failures such as:
  Password recovery
  Upload new IOS into router with No IOS installed
  Selecting a boot source and default boot filename
  Set console terminal baud rate to upload new IOS quicker
  Load operating software from ROM
  Enable booting from a TFTP server

## Slide 4: Getting to the ROM Monitor
Windows using HyperTerminal for the console session
  Ctrl-Break
FreeBSD/UNIX using Tip for the console session
  <Enter>, then ~# OR
  Ctrl-], then Break or Ctrl-C
Linux using Minicom for the console session
  Ctrl-A F

## Slide 5: Disaster Recovery: How to Recover a Lost Password
Connect your PC’s serial port to the router’s console port
Configure your PC’s serial port:
  9600 baud rate
  No parity
  8 data bits
  1 stop bit
  No flow control

## Slide 6: Disaster Recovery: How to Recover a Lost Password
Your configuration register should be 0x2102; use “show version” command to check
Reboot the router and apply the Break-sequence within 60 seconds of powering the router, to put it into ROMMON mode
  Rommon 1>confreg 0x2142
  Rommon 2>reset
  Router reboots, bypassing startup-config file (NVRAM)

## Slide 7: Disaster Recovery: How to Recover a Lost Password
  Type Ctrl-C to exit Setup mode
  Router>enable
  Router#conf m OR copy start run (only!!!)
  Router#show running OR write terminal
  Router#conf t
  Router(config)enable secret forgotten
  Router(config)int e0/0…
  Router(config-if)no shut
  Router(config)config-register 0x2102
  Router(config)Ctrl-Z or end
  Router#copy run start OR write memory
  Router#reload