## Slide 1: CCNA (200-125)
Backup & Recovery
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture Overview
TFTP Server
Cisco Router/Switch’s Backup
Cisco Router/Switch’s Upgrading/Recovery

## Slide 3
TFTP(Trivial File Transfer Protocol)
TFTP Server allows you to take backup, upload and save your IOS Image and current configuration on it.
TFTP Server is a software program of 1.3Mb. This should be installed on that TFTP server i.e., (Personnel Computer).
C:\Program files\cisco systems\cisco TFTP
Note: Always while taking Backup or Restoration TFTP software should execute on that particular computer.

## Slide 4
Backup Sources :
Through Telnet Session.
Through Console Session.
Through Auxillary Port (Remote Session)

## Slide 5
Backup of IOS Image
Router#Copy Flash:(Press Tab key) Tftp
Address or name of the remote host [ ]? (Ip address of tftp)
Destination file name [ ] ? (Press enter key or a name)
Backup of Configuration
Router#Copy Startup-config: Tftp
Address or name of the remote host [ ]? (Ip address of tftp)
Destination file name [ ] ? (Give a name)

## Slide 6
Upgrading IOS Image
Note: This process can only be done by Console Session.
Router#Copy tftp Flash:
Address or name of remote host []?
Source file name []?
Destination file name []?
Erase Flash: before copying [confirm]?
Erasing the Flash file system will remove all files: continue? [confirm]
Erasing device eeeeeeee……….eeeeeee.eee.eeee.ee
Loading!!!!!!!!!!!!!!!!!!!!!!!!!!!!!…….!!!!…….!!!!!!

## Slide 7
Recovery of Configuration File
Router#Copy tftp: running-config
Address or name of remote host []?
Source file name []?
Destination file name []?
….