## Slide 1: CCNA (200-125)
Switch Basics
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture Overview
Types of Switching / Methods
Collision Domain Vs. Broadcast Domain
Cisco Switch Password Recovery

## Slide 3: Types of Switching/Methods
There are four forwarding methods a bridge or switch can use;
Store and Forward
Cut Through
Fragment Free
Adaptive Switching

## Slide 4: Store and Forward
The Switch buffers a received frame and verifies each frame before forwarding it.
  Error Checking- A frame containing error is dropped.
  Error free frame is forwarded.
This method is slow as compared to other methods because of its error checking procedure but ensures the reliable data delivery.
Nowadays these types of switches are mostly used because they have efficient built-in technology / circuitry, and bandwidth is no more an issue.

## Slide 5: Cut through
This Switch reads only up to the frame’s hardware address before starting to forward it.
There is no error checking with this method
Fastest method of data transferring
Data delivery is not guaranteed
Delivered Frame may contain errors

## Slide 6: Fragment Free
A method that attempts to retain the benefits of both the methods (i.e. store and forward and cut through).
Fragment Free checks the first 64 bytes of the frame, where addressing information is stored.
According to Ethernet specifications;
  Collisions should be detected during the first 64 bytes of the frame, so frames that are in the error because of collision will not be forwarded.
  This way the frame will always reach its intended destination
  Error checking of the actual data in the packet is left for the end device.

## Slide 7: Adaptive Switching
A method of automatically selecting between the other three methods.

## Slide 8: Collision Domain vs. Broadcast Domain
Collision Domain:
  A network or a part of network where data collision can occur. OR
  Group of NIC in which collision can occur.
  Collision occurs when two or more devices send the packet at the same time on a shared network segment.
  Hub has one collision domain (maximum collisions), whereas in Switch each port is a separate collision domain (almost no collision)
Broadcast Domain:
  All nodes can reach each other by broadcast. OR
  Group of NIC, broadcast send by one, received by all others

## Slide 9: Password Recovery Steps for Cisco Catalyst Switches
Ever turn on a switch or perform a reload just to find out that you’ve accidentally been locked out of your networking device? Here is an easy way to physically perform a password recovery on a Cisco Catalyst Switch.
Step 1: Connect your PC or terminal into the switch console port with the blue console cable.
Step 2: Open up Putty, and select serial as connect type. Click open to get access to the switch.
Step 3: Unplug the power cable to the switch.

## Slide 10
Step 4:Press and hold the Mode button on the front of the switch and plug the power cable back into the switch at the same. After the power cable has been plugged in, wait a couple of seconds and then release the Mode button.
Step 5: Your display on your HyperTerminal should look like this… switch:
Step 6: Enter these commands into the switch
switch: flash _init
switch: load_helper
switch: dir flash:

## Slide 11
Directory of flash:
13 drwx 192 Mar 01 1993 22:30:48 c2960-mz-124-0.0.53.bin
11 -rwx 5825 Mar 01 1993 22:31:59 config.text
18 -rwx 720 Mar 01 1993 02:21:30 vlan.dat
switch: rename flash:config.text flash:config.text.old
switch: boot
Step 7: Once the switch reboots, answer NOto “Would you like to enter system configuration dialog? [Yes/No]:

## Slide 12
Step 8: Get into the privilege prompt.
Switch>enable
Switch#rename flash:config.text.old flash:config.text
Switch#copy flash:config.text system:running-config
Source filename [config.text]?
Destination filename [running-config]?
Press Enter to copy

## Slide 13
Step 9: Get into global configuration
Switch#conf t
Switch (config)#enable secret password
Enter the password you would like
Step 10: Return to Privilege mode and save your config
Switch (config)#exit
Switch#copy run start