## Slide 1: VLANS
Institute of IT Professionals
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture Overview
What is a VLAN?
VLAN Memberships
VLAN links
Frame tagging
VTP
Trunking
Configuring VLANs
Configuration examples

## Slide 3: VLANS (Virtual LANS)
Multiple LANs in a single LAN are created to overcome the major LAN Problems like;
  Broadcast Problem
  Security Problem
Broadcast is generated in a LAN generally as a result of ARP when the destination MAC is needed, or when a server advertising its services to its clients. In case of broadcast every node has to process.
VLANs are created to minimize the processing of extra nodes in order to make the boost up performance of a network.

## Slide 4: VLANS
Distributing broadcast domain in LAN
VLANS are created to make Logical grouping of different departments like HR, MKT, IT etc
Trunk Link belongs to all VLANs
All the ports are in VLAN1 by default

## Slide 5: Switches

## Slide 6: Features of VLANs
Simplify network management
Provides a level of security over a flat network
Flexibility and Scalability

## Slide 7: Broadcast Control
Broadcasts occur in every protocol
Bandwidth & Broadcasts
Flat network
VLANs & Broadcasts

## Slide 8: Flat Network Structure

## Slide 9: Security
Flat network problems
VLANs

## Slide 10: Flexibility & Scalability
Layer-2 switches only read frames
  Can cause a switch to forward all broadcasts
VLANs
  Essentially create broadcast domains
    Greatly reduces broadcast traffic
    Ability to add wanted users to a VLAN regardless of their physical location
    Additional VLANs can be created when network growth consumes more bandwidth

## Slide 11: Switched Network

## Slide 12: Physical LANs Connected To A Router

## Slide 13: VLANs Remove The Physical Boundary

## Slide 14: VLAN Memberships
Static VLANs
  Typical method of creating VLANs
  Most secure
    A switch port assigned to a VLAN always maintains that assignment until changed
Dynamic VLANs
  Node assignment to a VLAN is automatic
    MAC addresses, protocols, network addresses, etc
  VLAN Management Policy Server (VMPS)
    MAC address database for dynamic assignments
    MAC-address to VLAN mapping

## Slide 15: Identifying VLANs
Access links
  A link that is part of only one VLAN
Trunk links
  Carries multiple VLANs

## Slide 16: Identifying VLANs (cont.)

## Slide 17: Frame Tagging
Definition: A means of keeping track of users & frames as they travel the switch fabric & VLANs
  User-defined ID assigned to each frame
  VLAN ID is removed before exiting trunked links & access links

## Slide 18: VLAN ID Methods
Inter-Switch Link (ISL)
  Cisco proprietary
  FastEthernet & Gibabit Ethernet only
IEEE 802.1q
  Must use if trunking between Cisco & non-Cisco switch

## Slide 19: VLAN ID Methods
Protocols at Trunk Links:
  IEEE 802.1q or 802 dot1q:
  ISL (Interswitching Link)
  Frame tag=8 bytes
  Dot1q=12 bytes
Data
Tag
Data
Encapsulation

## Slide 20: VLAN ID Methods
Example;
Encapsulation on Trunk Link
802 dot1q
v2
v2
v8
Access Link
S1
S2

## Slide 21: Configuring VLANs
Creating VLANs
Assigning Switch Ports to VLANs
Configuring Trunk Ports
Configuring Inter-VLAN routing

## Slide 22: Configuring VLANs
Switch#show vlans
Switch#conf t
Switch (config): VLAN2
Switch (config-vlan): name IT
Switch (config-vlan):exit
Switch (config): VLAN3
Switch (config-vlan): name HR

## Slide 23: Configuring VLANs
Adding Ports into VLAN:
Switch(config)#interface fastethernet 0/2
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan2
Selecting Range of Ports:
Switch(config)#interface range fastethernet 0/2 - 10
Selecting Specific Ports:
Switch(config)#interface range fa0/2 , fa0/3 , fa0/5

## Slide 24: VTP (VLAN Trunking Protocol)

## Slide 25: VTP (VLAN Trunking Protocol)
Purpose: to manage all configured VLANs across a switch internetwork & maintain consistency
  Allows an administrator to add, delete, & rename VLANs
VTP send information of VLANs via trunk links to all other switches
To Synchronize the information to each other which are in same domain

## Slide 26: VTP Benefits
Benefits
  Consistent configuration
  Permits trunking over mixed networks
  Accurate tracking
  Dynamic reporting
  Plug-and-Play
A VTP server must be created to manage VLANs

## Slide 27: VTP Modes

## Slide 28: VTP Modes
VTP Server:
  Default for all Catalyst switches
  Minimum one server for a VTP domain
  Functions ;
    VTP Server can create VLANs
    Can Delete VLANs
    Can Modify VLANs

## Slide 29: VTP Modes
VTP Client:
  When one switch is configured as VTP server the remaining all are configured as VTP Client
  Receives information + sends/receives updates
  VTP client has no functionality like VTP Server.
  Cannot make any changes

## Slide 30: VTP Modes
VTP Transparent:
  It is having almost all the functionality of VTP server except it doesn’t synchronize its own information to other switches
  Does not participate in a VTP domain but forwards VTP advertisements
  Can add/delete VLANs
  Important Info:
    VTP Domain name must be same
    Password must be same

## Slide 31: Configuring VTP
Switches are configured to be VTP servers by default.