## Slide 1
ITP | Institute of IT Professionals
Inter VLAN Routing
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture Overview
What is Inter VLAN Routing?
Port based VLANS
Routed Ports
Configuring Inter VLAN Routing
  Using Multilayer Switch
  Using Router on a stick
Lab Examples/Practice

## Slide 3: What is Inter VLAN Routing?
Inter VLAN Routing
  Communication between different VLANs (networks)
  Different VLANs behave as if different networks (logically)
  Enable Routing /Inter VLAN Routing
  Using
    Multilayer Switch
    Router on a Stick

## Slide 4: Port-Based VLANs
  Add ports to a VLAN by using the switchport interface configuration commands:
    Identify the interface.
    For a trunk port, set trunk characteristics and define the VLANs to which it can belong.
    For an access port, set and define the VLAN to which it belongs.

## Slide 5: Switch Ports
  Layer 2-only interfaces associated with a physical port
  Access port
    Carries the traffic of and belongs to only one VLAN
  Trunk port
    Carries the traffic of multiple VLANs
    By default is a member of all VLANs in the VLAN database
  Configure switch ports using the switchport interface configuration commands

## Slide 6: Layer 3 Switch Virtual Interfaces
  Represent a VLAN of switch ports as one interface to the routing or bridging function in the system
  Created the first time that you enter the vlan interface configuration command for a VLAN interface
  Configure a VLAN interface for each VLAN for which you want to route traffic, and assign it an IP address
  Support routing protocol and bridging configurations

## Slide 7: Routed Ports
  Routed ports defined:
    Physical port that acts like a port on a router
    Not associated with a particular VLAN
  To configure a routed port:
    Enable IP routing within the switch.
    Put the interface into Layer 3 mode with the no switchport interface configuration command.
    Assign an IP address and subnet mask to the port.
    Assign routing protocol characteristics by enabling IP routing.

## Slide 8: Problem: Isolated Broadcast Domains
  Because of their nature, VLANs inhibit (prevent) communication between VLANs.
Notes: Purpose: This slide poses the problem of communicating between VLANs.
Emphasize:
Point out that VLANs, by their nature, are designed to keep data from traversing the VLAN borders.
However, end users stations need to communicate with entities outside the VLAN borders.
Use the example of end users in one VLAN needed to communicate with enterprise servers residing in a VLAN across the network core.
Transition: Following introduces the solution.

## Slide 9: Solution: Routing Between VLANs
  Communications between VLANs requires a Layer 3 services module.
Notes: Purpose: This slide introduces routers as the solution to inter-VLAN communications.
Emphasize:
In switched networks, route processors are used to provide communications between VLANs.
Before you can configure routing between VLANs, you must have defined the VLANs on the switches in your network.
Refer to the Cisco Internetworking Design Guide and appropriate switch documentation for information on these topics.
The Cisco Internetworking Design Guide is available from Cisco Press.
Inter-VLAN Routing is discussed in the Cisco IOS Switching Services Configuration Guide located on the Cisco Documentation CD-ROM.
Transition: Following begins the discussion of some problems that occur as result of inter-VLAN routing.

## Slide 10: Connecting VLANs with a Multilayer Switch

## Slide 11: Configuring Inter-VLAN Routing on a Layer3 Switch
Switch(config)#ip routing
Enables IP routing on the switch
Switch(config)#router ip_routing_protocol <options>
Specifies the IP routing protocol (optional command)
Switch(config)#interface vlan-id
Enters interface configuration mode for a specific VLAN
Switch(config-if)#ip address n.n.n.n subnet-mask
Assigns an IP address to the VLAN
Switch(config)#Vlan vlan-id
Create a VLAN

## Slide 12: Router on a stick

## Slide 13: Router with Individual VLAN associations

## Slide 14: Routing Between VLANs

## Slide 15: Router on a Stick
  The router can support a single trunk for multiple VLANs.
Notes: Purpose: This slide discusses the solution of ISL.
Emphasize:
The Inter-Switch Link (ISL) protocol is used to inter-connect two VLAN-capable Fast Ethernet devices, such as the Catalyst 5000 or Cisco 7500 routers. The ISL protocol is a packet-tagging protocol that contains a standard Ethernet frame and the VLAN information associated with that frame.
ISL is currently supported over Fast Ethernet links, but a single ISL link, or trunk, can carry traffic from multiple VLANs.
The concept of ISL was discussed in the “Defining Common Workgroups” chapter. How to configure ISL links is discussed later in this chapter.
Discuss the example in the SG.
Transition: Following is a discussion of ISL links to single router.

## Slide 16: Router on a Stick (Cont.)
  Advantages:
    Simple to implement using any combination of systems
    Router provides communications between VLANs on remote switches
  Disadvantages:
    Single point of failure if only one router is used
    Single traffic path can become congested
    Network topology can cause performance issues

## Slide 17: Router on a Stick Between VLANs with ISL Trunks
Notes: Purpose: This figure shows the configuration of the router on a stick.
Emphasize: Highlight the two different interconnecting networks, 10.1.1.0 and 10.2.2.0.

## Slide 18: Router on a Stick Between VLANs with 802.1Q Trunks
Notes: Purpose: This figure shows the configuration of the router on a stick.
Emphasize: Highlight the two different interconnecting networks, 10.1.1.0 and 10.2.2.0.

## Slide 19: Verifying Inter-VLAN Routing
  ping tests connectivity to remote hosts.
Notes: Purpose: This slide discusses the ping command.
Emphasize: Use the ping command to test connectivity to remote hosts.
The ping command will return one of the following responses:
  Success rate is 100 percent or ip address is alive. This response occurs in 1 to 10 seconds, depending on network traffic and the number of ICMP packets sent.
  Destination does not respond. No answer message is returned if the host does not
  Unknown host. This response occurs if the targeted host does not exit
  Destination unreachable. This response occurs if the default gateway cannot reach the specified network
  Network or host unreachable. This response occurs if there is no entry in the route table for the host or network.
You can also test the routes packets will take from the route processor to a specific destination by using the trace ip destination command.
For more information on the trace ip command, refer to the Cisco IOS Release 12.0 Command Summary .
Transition: Following is the visual for the laboratory exercise.

## Slide 20: Verifying the Inter-VLAN Routing Configuration
Switch#show running-config
Displays the current configuration
Switch#show ip route
Displays IP route table information
Switch#show ip protocols
Displays IP routing protocol information

## Slide 21: Lab Examples / Practice

## Slide 22: Lab#01: Scenario for Inter VLAN Routing

## Slide 23: Configuration
ON router (R1)
  Router (config) # Int e 0
  Router (config-if ) # No ip address
  Router (config-if ) # exit
  Router (config) # Int e 0/0.10
  Router (config-sub-if ) # Encapsulation dotlq 10
  Router (config-sub-if ) # Ip address 10.1.1.1 255.0.0.0
  Router (config-sub-if ) # exit
  Router (config) # Int e 0/0.20
  Router (config-sub-if ) # Encapsulation dotlq 20
  Router (config-sub-if ) # Ip address 20.1.1.1 255.0.0.0

## Slide 24
ON SW1
  Switch# vlan database
  Switch(vlan)# vlan 10 name sales
  Switch(vlan)# exit
  Switch# vlan database
  Switch(vlan)# vlan 20 name finance
  Switch(vlan)# exit
  Switch(config)# Int fa0/1
  Switch(config-if)# Switchport mode access
  Switch(config-if)# Switchport access vlan10
  Switch(config-if)# exit

## Slide 25
  Switch(config)# Int fa0/2
  Switch(config-if)# Switchport mode access
  Switch(config-if)# Switchport access vlan10
  Switch(config-if)# exit
  Switch(config)# Int fa0/3
  Switch(config-if)# Switchport mode access
  Switch(config-if)# Switchport access vlan20
  Switch(config-if)# exit
  Switch(config)# Int fa0/4
  Switch(config-if)# Switchport mode access
  Switch(config-if)# Switchport access vlan20
  Switch(config-if)# exit

## Slide 26
  Switch(config)# Int fa0/5
  Switch(config-if)# Shutdown
  Switch(config-if)# Switchport trunk encapsulation dot1q
  Switch(config-if)# Switchport mode trunk
  Switch(config-if)# Switchport nonegotiate
  Switch(config-if # No shutdown
  Switch(config-if)# exit

## Slide 27
Verification :
  Verify if PC’s in VLAN 10 can communicate with PC’s in VLAN 20 using Ping

## Slide 28: InterVLAN Configuration Example#2

## Slide 29: Example 3

## Slide 30: Example 4

## Slide 31: Example 5

## Slide 32: Configuring Switching In Our Sample Internetwork

## Slide 33: 2950C

## Slide 34: 2950B

## Slide 35: Setting Up Trunking

## Slide 36: Inter-VLAN communication