## Slide 1: STP, RSTP, Port Fast, Ether Channel
ITP|Institute of IT Professionals
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Lecture Overview
STP (Spanning Tree protocol)
Rapid STP
Ether Channel
Port Fast

## Slide 3: STP (Spanning Tree Protocol)
Spanning Tree Protocol (STP) uses Spanning Tree Algorithm to avoid the Switching loops in layer-2 devices (bridges or switches).
STP works when multiple switches are used with redundant links avoiding Broadcast Storms, Multiple Frame Copies & Database instability.
STP is a open standard (IEEE 802.1D)
STP is enabled by default on all Cisco Catalyst switches
STP blocks the ports which is responsible of making loops and ups the alternative port having the high / more bandwidth.

## Slide 4: STP Terminology
BPDU:
All switches exchange information through what is called as Bridge Protocol Data Units (BPDUs)
BPDUs contain a lot of information to help the switches determine the topolog and any loops that result from that topology.
BPDUs are sent every 2 sec
Bridge ID:
Each switch has a unique identifier called a Bridge ID or Switch ID
Bridge ID = Priority + MAC address of the switch
When a switch advertises a BPDU , they place their switch id in these BPDUs.

## Slide 5: STP Terminology
Root Bridge:
The bridge with the Best (Lowest) ID.
Out of all the switches in the network , one is elected as a root bridge that becomes the focal point in the network.
Non-Root bridge:
All Switches other than the Root Bridge are Non-Root Bridges
Designated port:
Either a port On a root bridge or a port that has been determined as having the best (lower) cost.
A designated port will always in Forward Mode

## Slide 6: STP Terminology
Root port:
The link directly connected to the root bridge, or the shortest path to the root bridge.
Priority and Alternatives if Conflict occurred.
  Root port with the least cost (Speed) connecting to the root bridge.
  The bridge with the Best (Lowest) Switch ID.
  Lowest Physical Port Number.
Only One root port will be in Bridge or switch.
Non Designated port:
All the Port or ports which are blocked by STP to avoid switching loop.
A Non Designated port Will Always in Blocked Mode.

## Slide 7: STP (Spanning Tree Protocol)
Parameters to select a root switch
  Bridge priority (32768) default.(0-61440)
  MAC address

## Slide 8: STP (Spanning Tree Protocol)
Bridge id is calculated.
  Bridge id=bridge priority + mac address.
Which ever the switch having least bridge ID will be elected as root Bridge and others are non-root bridge.
On root bridge the ports used for cascading are called designated ports. All the designated ports will be at forwarding state .
In non root bridge from the two ports one will be selected as root port. This will be depending on the cost speed).
least cost path (faster transmission) the other port will be blocked.

## Slide 9: STP (Spanning Tree Protocol)
BPDU (Bridge Protocol Data Unit):
The “hello” packets that are sent by root bridge for every 2 sec to inform that it is working properly are called BPDUS. If non root bridge do no receive 10 BPDUs for next 20secs then it is clear that the root bridge has failed.
Max age time: 20secs, Then a new root bridge is selected.
if switch A is selected as root bridge and ports 1 & 2 Of switch A are designated ports. Depending on the shortest paths for high speed & low cost one port of switch B is selected as root port & the other will be blocked.
Root port is selected on the basis of preferred BPDU.

## Slide 10: STP (Spanning Tree Protocol)
Typical Costs of Different Ethernet Networks
Lowest Path cost is preferred BPDU
If cost is same then, lowest switch id is checked
If above 2 criterian don’t meet then lowest port id is checked
Origional IEEE Cost | IEEE Cost | Speed New
1 | 2 | 10 GB
1 | 4 | 1 GB
10 | 19 | 100 MB
100 | 100 | 10 MB

## Slide 11: STP (Spanning Tree Protocol)
Example;
Root
4
4
4
4
8

## Slide 12: STP Port states
The ports on a switch with enabled STP are in one of the following five port states.
  Blocking 20 Sec or No Limits.
  Listening 15 Sec.
  Learning 15 Sec.
  Forwarding No Limits.
  Disable No Limits
A switch does not enter any of these port states immediately except the blocking state. When the Spanning Tree Protocol (STP) is enabled, every switch in the network starts in the blocking state and later changes to the listening and learning states.

## Slide 13: STP Port states
Blocking:
The Switch Ports will go into a blocking state at the time of election process, when a switch receives a BPDU on a port that indicates a better path to the root switch, and if a port is not a root port or a designated port.
A port in the blocking state does not participate in frame forwarding and also discards frames received from the attached network segment. During blocking state, the port is only listening to and processing BPDUs on its interfaces. After 20 seconds, the switch port changes from the blocking state to the listening state.
Listening:
After blocking state, a root port or a designated port will move to a listening state. All other ports will remain in a blocked state. During the listening state the port discards frames received from the attached network segment and it also discards frames switched from another port for forwarding. At this state, the port receives BPDUs from the network segment and directs them to the switch system module for processing. After 15 seconds, the switch port moves from the listening state to the learning state.

## Slide 14: STP Port states
Learning:
A port changes to learning state after listening state. During the learning state, the port is listening for and processing BPDUs. In the listening state, the port begins to process user frames and start updating the MAC address table. But the user frames are not forwarded to the destination. After 15 seconds, the switch port moves from the learning state to the forwarding state.
Forwarding:
A port in the forwarding state forwards frames across the attached network segment. In a forwarding state, the port will process BPDUs, update its MAC Address table with frames that it receives, and forward user traffic through the port. Forwarding State is the normal state. Data and configuration messages are passed through the port, when it is in forwarding state.
Disabled:
A port in the disabled state does not participate in frame forwarding or the operation of STP because a port in the disabled state is considered non-operational.

## Slide 15: STP (Spanning Tree Protocol)
Commands:
# show spanning-tree protocol  To show STP
# spanning-tree vlan 1 priority ? To set Bridge Priority
  (0-61440) with increment of 4096
0 4096 8192 1278 16384 ......... So on

## Slide 16: RSTP (Rapid Spanning Tree protocol)
In case the root port is down STP process is started once again & BPDUs are sent in order to select the other port as root port. This process will take 50 seconds.
  20 Sec (10 BPDUs) + 30 Sec (Forwarding Delay i.e Listening/Learning)
RSTP enable or up the alternative port within milliseconds. when RSTP runs first time, it decides about root switch, root port, and it also select its assistance alternate port. In the case root port is down it speedily up the alternative port within no time on the basis of previous BPDU, so the listening and learning process is not started once again. RSTP have proactive behiour.
Command;
Switch(config)# spanning tree mode rapid-pvst

## Slide 17: EtherChannels
EtherChannels consist of individual links bundled into a single logical link.
Combined the bandwith of individual links by adding into a channel group
Running STP we can enjoy the redudency and the maximum bandwidth
Provides fault tolerant high speed links between switches, routers, and servers.
Can provide full duplex bandwidth up to 800 Mbps.
EtherChannels can consist of up to eight interfaces.
7 Channel Groups maximum can be created
Ports to add into a chanel group must be of similar characteristics

## Slide 18: Ether Channels
You must manually assign an interface to an etherchannel using the channel-group command.
S1
S2

## Slide 19: Ether Channels
Protocols:
PAgP (Port Aggregation Protocol)
LACP (Link Aggregation Control Protocol)
Dynamically groups similarly configured interfaces into a single logical link

## Slide 20: Ether Channels
PAGP:
  PAgP has three modes: on, auto, and desirable.
  PAgP is cisco properietry protocol
LACP:
  Works on non-cisco devices
  Modes are active, passive, on

## Slide 21: EtherChannel Commands
Switch(config)#inferface range fa 0/1 - 3
Switch(config-if)#channel-group 1 mode desirable
Show etherchannel summary
Show etherchannel protocol
Show etherchannel port
Show etherchannel details

## Slide 22: Port Fast
Port States:
  Blocking 20 sec
  Listening 15 sec
  Learning 15 sec
  Disabled no limit (Logically down)
  Forwarding Data forwarding starts after root port is selected
Forwarding Delay:
When STP process is running and until finished, the ports are in the blocking, listening, learning states, forwarding of data doesn’t start. Data Forwarding starts after 50 seconds, thats why this time is called forwarding delay.
Port Fast:
The port is up before listening & learning process, so there is no forwading delay. The ports that are not the part of STP process usually access ports, are set to port fast. Access ports don’t need to recieve BPDUs.

## Slide 23: Port Fast
Commands;
Switch(config)# interface fa 0/5
Switch(config-if)# spanning tree portfast
For range of interfaces
Switch(config)# interface range fa 0/5-10
Switch(config-range)# spanning tree portfast