## Slide 1: CCNA (200-125)
High Availability and Redundancy
(VRRP, GLBP)
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Objectives:
High Availability
Layer 3 Redundancy Protocols
  HSRP (Hot Standby Router Protocol)
  VRRP (Virtual Router Redundancy Protocol)
  GLBP (Global Load Balancing Protocol)

## Slide 3: VRRP
Very similar to HSRP in terms of configurations and working.
The main difference is that HSRP is Cisco Proprietary but VRRP is industry standard
Timers have been decreased, fast convergence.
A group of routers function as one virtual router by sharing ONE virtual IP address and ONE virtual MAC address
One (master) router performs packet forwarding for local hosts
The rest of the routers act as “back up” in case the master router fails
Backup routers stay idle as far as packet forwarding from the client side is concerned
Notes: In HSRP, both the active and standby routers send periodic messages (known as hello messages). In VRRP, only the master sends periodic messages (known as advertisements).
Same problem with load balancing requirements.
Cisco developed HSRP in response to emerging customer requirements. The company continues to enhance its capability based on customer feedback and market direction. Widely deployed by many Cisco customers, HSRP is a time-proven feature of Cisco IOS software. It has some great benefits like HSRP tracking and preempt feature which is not available in standardized VRRP.
However we strive to be standards compliant and therefore we are in the process of supporting VRRP. VRRP is also something which will be useful interoperating with 3rd party switches for gateway redundancy.

## Slide 4: VRRP: Configuration
On Router-1(master)
R1(config)# int f0/0
R1(config-if)# ip add 192.168.1.1 255.255.255.0
R1(config-if)# vrrp 5 ip 192.168.1.1
On Router-2 (backup)
R2(config)# int f0/0
R2(config-if)# ip add 192.168.1.2 255.255.255.0
R2(config-if)# vrrp 5 ip 192.168.1.1

## Slide 5: First Hop Redundancy with VRRP
Gateway routers
CL1
CL2
CL3
VRRP ACTIVE
VRRP BACKUP
VRRP BACKUP
Clients
R1
R2
R3
R1- Master, forwarding traffic; R2, R3 - backup
IP: 10.0.0.254
MAC: 0000.0c12.3456
vIP: 10.0.0.10
vMAC: 0000.5e00.0100
IP: 10.0.0.253
MAC: 0000.0C78.9abc
vIP:
vMAC:
IP: 10.0.0.252
MAC: 0000.0cde.f123
vIP:
vMAC:
IP: 10.0.0.1
MAC: aaaa.aaaa.aa01
GW: 10.0.0.10
ARP: 0000.5e00.0100
IP: 10.0.0.2
MAC: aaaa.aaaa.aa02
GW: 10.0.0.10
ARP: 0000.5e00.0100
IP: 10.0.0.3
MAC: aaaa.aaaa.aa03
GW: 10.0.0.10
ARP: 0000.5e00.0100
Notes: Same problem with load balancing requirements…only 1 router is active forwarding traffic from the client subnet to outside.

## Slide 6: GLBP (Gateway Load Balancing Protocol)

## Slide 7: GLBP
Cisco proprietary protocol
Provides Router redundancy with load balancing
Routers group together to work as one virtual router
Group is identified by Group ID
    Range 0 – 1024 (default is 0)
Group have two type of router
    AVG
    AVF
Copyright Zoom Technologies ®

## Slide 8: GLBP
AVG
    Active Virtual Gateway
    Reply for ARP coming for Virtual IP
    Divides load among AVF
    One Per group
AVF
    Active Virtual Forwarder
    Forwards user traffic coming for Virtual MAC
    They can be up to four forwarder per group
Copyright Zoom Technologies ®

## Slide 9: GLBP Elections
GLBP have two elections per Group
    Active Virtual Gateway
      Router with Highest Priority (default 100)
      Router with Highest Physical IP
      Only one AVG Per group
      Election are non-preemptive
    Active Virtual Forwarder
      Router with Highest weight (default 100)
      Router with Highest Physical IP
      Up to four AVF Per group
      Election are preemptive
Copyright Zoom Technologies ®

## Slide 10: GLBP Defined
A group of routers function as one virtual router by sharing ONE virtual IP address but using Multiple virtual MAC addresses for traffic forwarding
Provides uplink load-balancing as well as first hop fail-over
IP Leadership feature

## Slide 11: GLBP Requirements
Allow traffic from a single common subnet to go through multiple redundant gateways using a single virtual IP address
Provide upstream load-balancing by utilizing the redundant up-links simultaneously
Eliminate the need to create multiple vLANs or manually divide clients for multiple gateway IP address assignment
Preserve the same level of first-hop failure recovery capability as provided by HSRP

## Slide 12: First Hop Redundancy with GLBP
Gateway routers
CL1
CL2
CL3
GLBP AVG/AVF,SVF
GLBP AVF,SVF
GLBP AVF,SVF
Clients
R1
R2
R3
R1- AVG; R1, R2, R3 all forward traffic
IP: 10.0.0.254
MAC: 0000.0c12.3456
vIP: 10.0.0.10
vMAC: 0007.b400.0101
IP: 10.0.0.253
MAC: 0000.0C78.9abc
vIP: 10.0.0.10
vMAC: 0007.b400.0102
IP: 10.0.0.252
MAC: 0000.0cde.f123
vIP: 10.0.0.10
vMAC: 0007.b400.0103
IP: 10.0.0.1
MAC: aaaa.aaaa.aa01
GW: 10.0.0.10
ARP: 0007.B400.0101
IP: 10.0.0.2
MAC: aaaa.aaaa.aa02
GW: 10.0.0.10
ARP: 0007.B400.0102
IP: 10.0.0.3
MAC: aaaa.aaaa.aa03
GW: 10.0.0.10
ARP: 0007.B400.0103
Notes: A redundancy group will consist of one virtual IP address and multiple virtual MAC addresses
Three main functions:
Active Virtual Gateway responds to all ARP requests with the designated virtual MAC address according to the load balancing algorithm.
Each member of the group monitors state of other member gateways. In the event of failure, a secondary virtual forwarder takes over for traffic destined to a virtual MAC impacted by the failure.
Default load balancing algorithm AVG uses to assign virtual mac to clients is round-robin. Others are host-dependent and Weighted.
Benefits: Simplified configuration, less administration, increased throughput in non-failure conditions.

## Slide 13: Campus Access Layer Design
Campus Network
GW= 10.88.50.10
GW= 10.88.49.10
C
C
A
A
A
D
D
B
B
Layer-3 switches at distribution layer
Layer-2 switches at access layer
Better utilization of resources and uplinks
GLBP balances traffic across both layer-3 switches
10.88.49.10
10.88.50.10
vIP address
vMAC A
vMAC C
vMAC B
vMAC D
Notes: These next few slides show some typical design where GLBP can be used.
Here you see a diagram of a typical campus with access and distribution layer. You could use GLBP in the layer 3 switches to load balance traffic from end stations on a common IP subnet.
All devices within a subnet could point to a common default gateway, 10.88.49.10.
Traffic would be handled by each layer-3 switch on a per-host basis.
Tip: Set the layer-2 CAM entry aging time in distribution layer switches to the same duration as the ARP timeout. This will minimize any flooding of IP unicast traffic upon expiration for traffic that is never received for a given MAC.
set cam agingtime 1-1000 14400
Will set the time to 4 hours, same as default ARP cache timeout for MSFC

## Slide 14: Service Provider Edge
10.88.49.10
10.88.50.10
vIP address
GW= 10.88.49.10
C
C
A
A
D
D
B
B
Redundant
CPE routers
Layer-2 switches at access layer
Better utilization of resources and uplinks
GLBP balances traffic across both routers
SP Network
High Availability for Remote Office
GW= 10.88.50.10
vMAC A
vMAC C
vMAC B
vMAC D
Notes: Here you see a diagram of a typical remote office with redundant CPE routers and links to a service provider network.
You could use GLBP in the routers to load balance traffic from end stations on a common IP subnet. You could use one IP subnet per wiring closet switch.
All devices on a switch could point to a common default gateway.
Traffic would be handled by each router on a per-host basis.
The benefit is that you can now use both links concurrently with simplified configuration.

## Slide 15: GLBP
B
C
E
D
IP 192.168.1.100
IP 192.168.1.200
IP 192.168.1.1
IP 192.168.2.1
IP 192.168.2.200
GW 192.168.1.150
IP 192.168.1.2
GW 192.168.1.150
X
Y
AVG/AVF
AVF
V-IP 192.168.1.150
Copyright Zoom Technologies ®
Notes: GLBP Communication Hello 3 Sec, 224.0.0.102, UDP 3222
GLBP Feature.
Load sharing
Multiple Virtual Router 1024 (Group) 4 VRF
preemption

## Slide 16: GLBP
B
C
E
D
IP 192.168.1.100
IP 192.168.1.200
IP 192.168.1.1
IP 192.168.2.1
IP 192.168.2.200
GW 192.168.1.150
IP 192.168.1.2
GW 192.168.1.150
X
Y
ARP
IP MAC
1.150-0000.0c00.0001
ARP
IP MAC
1.150 - 0000.0c00.0002
IP 192.168.1.200
AVG/AVF
V-IP 192.168.1.150
V-MAC 0000.0c00.0001
AVF
V-MAC 0000.0c00.0002
Notes: 0007.b4yy.yyyy
where yy.yyyy equals the lower 24 bits; these bits consist of 6 zero bits, 10 bits that
correspond to the GLBP group number, and 8 bits that correspond to the virtual
forwarder number
0007.b400.0102 : last 24 bits = 0000 0000 0000 0001 0000 0010 = GLBP group 1,
forwarder 2

## Slide 17: GLBP
B
C
E
D
IP 192.168.1.100
IP 192.168.1.200
IP 192.168.1.1
IP 192.168.2.1
IP 192.168.2.200
GW 192.168.1.150
IP 192.168.1.2
GW 192.168.1.150
X
Y
IP MAC
1.150 – 0000.0c00.0001
IP MAC
1.150 - 0000.0c00.0002
IP 192.168.1.200
AVG/AVF
V-IP 192.168.1.150
V-MAC 0000.0c00.0001
AVF
V-MAC 0000.0c00.0002
253

## Slide 18: GLBP
B
C
E
D
IP 192.168.1.100
IP 192.168.1.200
IP 192.168.1.1
IP 192.168.2.1
IP 192.168.2.200
GW 192.168.1.150
IP 192.168.1.2
GW 192.168.1.150
X
Y
IP MAC
1.150 – 0000.0c00.0001
IP MAC
1.150 - 0000.0c00.0002
IP 192.168.1.200
AVG/AVF
V-IP 192.168.1.150
V-MAC 0000.0c00.0001
AVF
V-MAC 0000.0c00.0002
253
V-MAC 0000.0c00.0001

## Slide 19: GLBP-Configurations