## Slide 1: CCNA (200-125)
IPv6 ROUTING
Instructor:
  Muhammad Naeem
  (MSIT/RHCE/CCNP/CCNA/MCSE)
  Cell: 0345-5238281
  E-Mail: mna571@yahoo.com

## Slide 2: Objectives: IPv6 Routing Prototocols
IPv6 Routing Types
  Static
  RIPng (RFC 2080)
  OSPFv3 (RFC 2740)
  IS-IS for IPv6
  MP-BGP4 (RFC 2545/2858)
  EIGRP for IPv6
  The IPv6 unicast-routing command is required to enable IPv6 before any routing protocol is configured.

## Slide 3: RIPng
Similar to IPv4
  Distance Vector
  Radius of 15 hops
  Split horizon
  Poison Reverse
  Based on RIPv2
  Updated
  IPv6 prefix, next hop IPv6 address
  Multicast group of FF02::9 the all rip routers multicast group as the destination for RIP updates
  IPv6 used for transport

## Slide 6: IPv6 basic configuration
On Router1: ------------------ R1(config)# ipv6 unicast-routing R1(config)# int f0/0 R1(config-if)# ipv6 add 2001:1:1:1::1/64 R1(config-if)# no shut R1(config-if)# int s0/0 R1(config-if)# ipv6 add 2001:1:1:2::1/64 | On Router2: ----------------- R2(config)# ipv6 unicast-routing R2(config)# int f0/0 R2(config-if)# ipv6 add 2001:1:1:3::1/64 R2(config-if)# no shut R2(config-if)# int s0/0 R2(config-if)# ipv6 add 2001:1:1:2::2/64

## Slide 8: OSPFv2 vs OSPFv3

## Slide 11: OSPFv3: Lab Scenario